ANNA Programming Card

| Opcode | Op | Operands | Description |
| --- | --- | --- | --- |
| 0000 | add | Rd Rs1 Rs2 | Two's complement addition: R(Rd) ( R(Rs1) + R(Rs2) |
| 0001 | sub | Rd Rs1 Rs2 | Two's complement subtraction: R(Rd) ( R(Rs1) – R(Rs2) |
| 0010 | and | Rd Rs1 Rs2 | Bitwise and operation: R(Rd) ( R(Rs1) & R(Rs2) |
| 0011 | or | Rd Rs1 Rs2 | Bitwise or operation: R(Rd) ( R(Rs1) ¦ R(Rs2) |
| 0100 | not | Rd Rs1 | Bitwise not operation: R(Rd) ( ~R(Rs1) |
| 0101 | shf | Rd Rs1 Imm6 | Bit shift. The contents of Rs1 are shifted left (if Imm6 is positive) or right with zero extension (if Imm6 is negative). The shift amount is abs(Imm6); the result is stored in R(Rd). |
| 0110 | lli | Rd Imm8 | The lower bits (7-0) of Rd are copied from Imm8. The upper bits (15-8) of Rd are equal to bit 7 of Imm8 (sign extension). |
| 0111 | lui | Rd Imm8 | The upper bits (15- 8) of Rd are copied from Imm8. The lower bits (7-0) of Rd are unchanged. |
| 1000 | lw | Rd Rs1 Imm6 | Loads word from memory using the effective address computed by adding Rs1 with the signed immediate: R(Rd) ( M[R(Rs1) + Imm6] |
| 1001 | sw | Rd Rs1 Imm6 | Stores word into memory using the effective address computed by adding Rs1 with the signed immediate: M[R(Rs1) + Imm6] ( R(Rd) |
| 1010 | bez | Rd Imm8 | Conditional branch – compares Rd to zero. If Rd is zero, then branch is taken with indirect target of PC + 1 + Imm8 as next PC. Immediate is a signed value. |
| 1011 | bgz | Rd Imm8 | Conditional branch – compares Rd to zero. If Rd is greater than zero, then branch is taken with indirect target of PC + 1 + Imm8 as next PC. Immediate is a signed value. |
| 1100 | addi | Rd Rs1 Imm6 | Add immediate: R(Rd) ( R(Rs1) + Imm6 |
| 1101 | jalr | Rd Rs1 | Jumps to the address stored in register Rd and stores PC + 1 in register Rs1. |
| 1110 | in | Rd | Input instruction: R(Rd) ( input |
| 1111 | out | Rd | Output instruction: output ( R(Rd). If Rd is r0, halts the processor. |
| Assembler Directives | .halt |  | Assemble directive that emits an out instruction (0xF000) that halts the processor. |
|  | .fill | Imm16 | Assembler directive that fills next memory location with the specified value. Immediate is a signed value. |

Registers

- Represented by fields Rd, Rs1, and Rs2.

- A register can be any value from: r0, r1, r2, r3, r4, r5, r6, r7.

- Register r0 is always zero.  Writes to register r0 are ignored.

Immediates

- Represented by fields Imm6, Imm8, and Imm16.  The number refers to the size of the immediate in bits.

- Immediates are represented using decimal values, hexadecimal values, or labels.  Hexadecimal values must start with '0x' and labels must be preceded with '&'.

- The immediate fields represent an unsigned value. The immediate field for lui is specified using a signed value but the sign is irrelevant as the eight bits are copied directly into the upper eight bits of the destination register.

- Labels refer to the address of the label.  If a label is used in a branch, the proper PC-relative offset is computed and used as the immediate.

Comments

- A comment begins with a pound sign '#' and continues until the following newline.

Labels

- Label definitions consist of a string of letters, digits, and underscore characters followed by a colon. The colon is not part of the label name.

- A label definition must precede an instruction on the same line.

- A label may only be defined once in a program. Only one label is allowed per instruction.  The instruction must appear on the same line as the label.

Instruction Formats

Instructions adhere to one of the following three instruction formats:

R-type (add, sub, and, or, not, jalr, in, out)

| 15 |  |  | 12 | 11 |  | 9 | 8 |  | 6 | 5 |  | 3 | 2 |  | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Opcode | Rd | Rs1 | Rs2 | Unused |

I6-type (addi, shf, lw, sw)

| 15 |  |  | 12 | 11 |  | 9 | 8 |  | 6 | 5 |  |  |  |  | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Opcode | Rd | Rs1 | Imm6 |

I8-type (lli, lui, bez, bgz)

| 15 |  |  | 12 | 11 |  | 9 | 8 | 7 |  |  |  |  |  |  | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Opcode | Rd | Unused | Imm8 |